## Slide 1: Challenge #8
By :
Yang Wu
Chuang Ding
Deepshikha Moolchandani​
Zhenyang Wu​
Diana Bayoumi

## Slide 2: Remote Control and Motion Detection
Installed Motion Software Package on Raspberry Pi which helps provide web cam stream to the IP address of the Pi.
Raspberry Pi linked to Arduino via USB.
Socket IO send the message to Node.js which sends message to Arduino via Serial Port.

## Slide 3: Remote Control Data Flow
Link Raspberry Pi to Arduino via USB
Socket IO send the message to Node.js
Node.js sends message to Arduino via Serial Port
Connect to Server.
Web cam stream to IP address of Pi.
Use SVG for visualization of dynamic location

## Slide 4: Localization
API mode (Enabled 2) configuration for all Xbees.
Collection of RSSI values in a lookup table from all 4 Beacons
Utilized KNN Algorithm to locate Xbee on the-go by comparing the sampled RSSI values to those of the lookup table
Use of SVG to dynamically visualize the transfer of the on the-go Xbee
Included Plan for the area with 29 partitions as our base areas for positioning our mobile query

## Slide 5: Localization Data Flow
Divide room in 29 Partitions.
4 Beacons collect RSSI values
API packets containing RSSI values sent to coordinator at Raspberry pi.
Implement KNN.
Connect to Server.
Use SVG for visualization of dynamic location

## Slide 6: Design Decisions for Autonomous
Use of 2 Lidar Lite sensors on the sides to implement turning at waypoints and IR sensors on the front for keeping distance from the wall.
Use of PID to control Epsilon Limit.
4 Arduinos / Xbee utilized as Beacons and a mobile Xbee as the query point that we want to localize.
Use of RSSI values gathered in vector format by sending packets through node.js in estimating the location of Crawler.

## Slide 7: Autonomous Data Flow
Initialize the crawler. And calibrate ESC
Initialize Lidar Lite sensors to control turning.
If Measured distance > Calibrated distance (400”)
Turn Right
PID to move in Straight Line within Epsilon (50cm)
Feedback loop in code to control the position.
IR Sensors : Stop at 20 cm from wall, back up and turn Right.Enable
Demo