## Slide 1: Challenge #7
By :
Yang Wu
Chuang Ding
Deepshikha Moolchandani​
Zhenyang Wu​
Diana Bayoumi

## Slide 2: Design Decisions
Use of 2 Lidar Lite sensors on the sides to implement turning at waypoints and IR sensors on the front for keeping distance from the wall.
Use of PID to control Epsilon Limit.
4 Arduinos / Xbee utilized as Beacons and a mobile Xbee as the query point that we want to localize.
Use of RSSI values gathered in vector format by sending packets through node.js in estimating the location of Crawler.

## Slide 3: FEATURES
API mode (Enabled 2) configuration for all Xbees.
Collection of RSSI values in a lookup table from all 4 Beacons
Utilized KNN Algorithm to locate Xbee on the-go by comparing the sampled RSSI values to those of the lookup table
Use of SVG to dynamically visualize the transfer of the on the-go Xbee
Included Plan for the area with 29 partitions as our base areas for positioning our mobile query

## Slide 4: AUTONOMOUS CAR CONTROLLER
Initialize the crawler. And calibrate ESC
Initialize Lidar Lite sensors to control turning.
If Measured distance > Calibrated distance (400”)
Turn Right
PID to move in Straight Line within Epsilon (50cm)
Feedback loop in code to control the position.
IR Sensors : Stop at 20 cm from wall, back up and turn Right.Enable
Demo

## Slide 5: LOCALIZATION DATA FLOW
Divide room in 29 Partitions.
4 Beacons collect RSSI values
API packets containing RSSI values sent to coordinator at Raspberry pi.
Implement KNN.
Connect to Server.
Use SVG for visualization of dynamic location

## Slide 6: CHALLENGES
Improving Accuracy of the crawler moving in straight line within epsilon limit.
Shortening Latency